## Slide 1: MQTT
國立中正大學資工系 黃仁竑教授

## Slide 2: What is MQTT ?
MQTT = MQ Telemetry Transport
MQTT protocol is a lightweight publish/subscribe protocol flowing over TCP/IP for remote sensors and control devices through low bandwidth, unreliable or intermittent communications.
MQTT was developed by Andy Stanford-Clark of IBM, and Arlen Nipper of Cirrus Link Solutions more than a decade ago.
ISO/IEC 20922:2016 Message Queuing Telemetry Transport (MQTT) v3.1.1. (Draft of v5.0 published in July, 2017)
Client libraries are available in almost all popular languages now.
  https://eclipse.org/paho/
The current MQTT specification is available at:
  http://docs.oasis-open.org/mqtt/mqtt/v3.1.1/mqtt-v3.1.1.html
  http://docs.oasis-open.org/mqtt/mqtt/v5.0/mqtt-v5.0.html

## Slide 3: Projects that Implement MQTT
Amazon Web Services announced Amazon IoT based on MQTT in 2015
Microsoft Azure IoT Hub uses MQTT as its main protocol for telemetry messages
Node-RED supports MQTT nodes as of version 0.14
Facebook has used aspects of MQTT in Facebook Messenger for online chat
The EVRYTHNG IoT platform uses MQTT as an M2M protocol for millions of connected products.

## Slide 4: Features of MQTT
It supports publish/subscribe message pattern to provide one-to-many message distribution and decoupling of applications
A messaging transport that is agnostic to the content of the payload
Three qualities of service for message delivery:
  "At most once" , where messages are delivered according to the best efforts of the operating environment. Message loss can occur. This level could be used, for example, with ambient sensor data where it does not matter if an individual reading is lost as the next one will be published soon after.
  "At least once", where messages are assured to arrive but duplicates may occur.
  "Exactly once", where message are assured to arrive exactly once. This level could be used, for example, with billing systems where duplicate or lost messages could lead to incorrect charges being applied.
A small transport overhead and protocol exchanges minimized to reduce network traffic.
A mechanism to notify interested parties when an abnormal disconnection occurs. (Last Will and Testament)
Notes: Testament遺囑

## Slide 5: Last Will and Testament
The protocol provides a method for detecting when clients close their connections improperly by using keep-alive packets.
  So when a client crashes or it’s network goes down, the broker can take action.
Clients can send a Last Will and Testament (LWT) message to the broker at any point. When the broker detects the client has gone offline (without closing their connection), it will send out the saved LWT message on a specified topic, thus letting other clients know that a node has gone offline unexpectedly.

## Slide 6: MQTT Pub/Sub Protocol
MQ Telemetry Transport (MQTT) is a lightweight broker-based publish/subscribe messaging protocol.
MQTT is designed to be open, simple, lightweight and easy to implement.
  These characteristics make MQTT ideal for use in constrained environments, for example in IoT.
    Where the network is expensive, has low bandwidth or is unreliable
    When run on an embedded device with limited processor or memory resources;
A small transport overhead (the fixed-length header is just 2 bytes), and protocol exchanges minimized to reduce network traffic
Source: MQTT V3.1 Protocol Specification, IBM, http://public.dhe.ibm.com/software/dw/webservices/ws-mqtt/mqtt-v3r1.html

## Slide 7: Suitable for Constrained Networks
Protocol compressed into bit-wise headers and variable length fields.
Smallest possible packet size is 2 bytes
Asynchronous bidirectional “push” delivery of messages to applications (no polling)
Client to server and server to client
Supports always-connected and sometimes-connected models
Provides Session awareness
Configurable keep alive providing granular session awareness
“Last will and testament” enable applications to know when a client goes offline abnormally
Typically utilzes TCP based networks e.g. Webscokets
Tested on many networks

## Slide 8: Publish Subscribe Messaging
A Publish Subscribe messaging protocol allowing a message to be published once and multiple consumers (applications / devices) to receive the message providing decoupling between the producer and consumer(s)
  A producer sends (publishes) a message (publication) on a topic (subject)
  A consumer subscribes (makes a subscription) for messages on a topic (subject)
  A message server/broker matches publications to subscriptions
    If no matches the message is discarded
    If one or more matches the message is delivered to each matching subscriber/consumer

## Slide 9: Broker/Publish/Subscribe
https://zoetrope.io/tech-blog/brief-practical-introduction-mqtt-protocol-and-its-application-iot/

## Slide 10: Publish Subscribe Messaging
A topic forms the namespace
  Is hierarchical with each “sub topic” separated by a /
    <country>/<region>/<town>/<postcode>/<house>/alarmState
A subscriber can subscribe to an absolute topic or can use wildcards:
  Single-level wildcards “+” can appear anywhere in the topic string
    sensors/+/uk/london/baker_street
    get data from all sensor types in London
  Multi-level wildcards “#” must appear at the end of the string
    sensors/temperature/uk/#
    Get temperature data from all locations in UK

## Slide 11: Publish Subscribe Messaging
A subscription can be durable or non durable
  Durable:
    Once a subscription is in place, a broker will forward matching messages to the subscriber:
      Immediately if the subscriber is connected
      If the subscriber is not connected, messages are stored on the server/broker until the next time the subscriber connects
  Non-durable: The subscription lifetime is the same as the time the subscriber is connected to the server / broker
A publication may be retained
  A publisher can mark a publication as retained
  The broker / server remembers the last known good message of a retained topic
  The broker / server gives the last known good message to new subscribers
    i.e. the new subscriber does not have to wait for a publisher to publish a message in order to receive its first message

## Slide 12: Publish/Subscribe
https://www.slideshare.net/michaeljohnkoster/mqtt-rest-bridge

## Slide 13: MQTT Message Format
Structure of an MQTT Control Packet
  The message header for each MQTT command message contains a fixed header.
  Some messages also require a variable header and a payload.
Fixed header, present in all MQTT Control Packets
Variable header, present in some MQTT Control Packets
Payload, present in some MQTT Control Packets

## Slide 14: MQTT Message Format
The format for fixed header:
DUP: Duplicate delivery of a PUBLISH Control Packet
QoS: Quality of Service
RETAIN: RETAIN flag
  This flag is only used on PUBLISH messages. When a client sends a PUBLISH to a server, if the Retain flag is set (1), the server should hold on to the message after it has been delivered to the current subscribers.
  This allows new subscribers to instantly receive data with the retained, or Last Known Good, value.

## Slide 15: Control Packet types
CONNECT: Client request to connect to Server
CONNACK: Connect acknowledgment
PUBLISH: Publish message
PUBACK: Publish acknowledgment
PUBREC: Publish received (assured delivery part 1)
PUBREL: Publish release (assured delivery part 2)
PUBCOMP: Publish complete (assured delivery part 3)

## Slide 16: Control Packet types
SUBSCRIBE: Client subscribe request
SUBACK: Subscribe acknowledgment
UNSUBSCRIBE: Unsubscribe request
UNSUBACK: Unsubscribe acknowledgment
PINGREQ: PING request
PINGRESP: PING response
DISCONNECT: Client is disconnecting

## Slide 17: QoS
QoS Level 0:
  No acknowledgment from the client and the reliability will be the same as that of the underlying network layer, TCP/IP.
QoS Level 1:
  This ensures that the message is delivered to the client at least once, but it could be delivered more than once. It relies on the client sending an ACK packet when it receives a packet.
QoS Level 2:
  This ensures that a message is delivered once and only once. This method requires an exchange of four packets, and will decrease performance of the broker. This level is also often left out of MQTT implementations due to its relative complexity.

## Slide 18: QoS
https://zoetrope.io/tech-blog/brief-practical-introduction-mqtt-protocol-and-its-application-iot/

## Slide 19: Variable Header
CONNECT packet
  Client requests a connection to a Server
  Fixed header: packet type=1
  Variable header: Protocol Name, Protocol Level (4), Connect Flags, Keep Alive
Connect Flags
If the Will Flag is set to 1 this indicates that, if the Connect request is accepted, a Will Message MUST be stored on the Server and associated with the Network Connection. The Will Message MUST be published when the Network Connection is subsequently closed.
  Client crashes without sending a DISCONNECT Packet first
Bit | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
 | User Name Flag | Password Flag | Will Retain | Will QoS |  | Will Flag | Clean Session | Reserved

## Slide 20: Payload
CONNECT packet
  Client Identifier
  Will Topic
  Will Message
  User Name
  User Password

## Slide 21: Security
Authentication
  Username and password as part of CONNECT action
Encryption
  SSL and plain text communication over TCP/IP
Broker
MQTT Client
authentication module
Queue
manager
Username/password
Username/password
Replied with
Yes/No

## Slide 22: Broker Software
Mosquitto - One of the earliest production ready brokers, Mosquitto is written in C and offers high performance with a lot of configurability.
Mosca - Written in Node.js, this can be embedded in a Node application or run as a standalone executable. Easy configuration and extensibility, also very performant.
RSMB - IBM’s implementation of the MQTT protocol. This is one of the less popular options but is a mature system, written in C.
HiveMQ - HiveMQ is a relatively new player, and is oriented towards enterprise environments.